## Slide 1: Agenda 10/21
Welcome and Q&A
Course objectives review
Lecture – Wide Area Networks (Chapter 10)
Quiz 5 – Chapters 8 and 9
Reminder – Assignment # 6 due tonight, Final Exam next week

## Slide 2: Wide Area Networks
Chapter 10
Panko and Panko
Business Data Networks and Security, 9th Edition
© 2013 Pearson

## Slide 3
LANs, MANs, and WANs
Access Lines
The Network Core
Using the Internet for Wide Area Networking
Cellular Data Service
Virtual WANs

## Slide 4: 10.1: LANs, MANs, and WANs
Local Area Networks (LANs)
  On the customer premises
Wide Area Networks (WANs)
  Connect sites across a region, country, the world
Metropolitan Area Networks (MANs)
  Connect sites in a single metropolitan area (a city and its suburbs)
  A type of WAN

## Slide 5: 10.1: LANs, MANs, and WANs
 | LAN | MAN | WAN
Implementation | Self | Carrier | Carrier
Ability to choose technology | High | Low | Low
Who manages the network? | Self | Carrier | Carrier

## Slide 6: 10.1: LANs, MANs, and WANs
 | LAN | MAN | WAN
Price | Highly related to cost | Highly unpre-dictable | Highly unpre-dictable
Cost per bit transmitted | Low | Medium | High
Therefore, typical speed range | 100 Mbps to 1 Gbps or more | 10 to 100 Mbps | 1 to 50 Mbps

## Slide 7: 10.1: LANs, MANs, and WANs
 | LAN | MAN | WAN
Can use switched technology? | Yes | Yes | Yes
Can use routed technology? | Yes | Yes | Yes

## Slide 8: 10.2: Single Networks versus Internets
Technology | LAN | WAN
Can be a single switched or wireless network? | Yes | Yes
Can be an internet? | Yes | Yes

## Slide 9: 10.3: Components of a WAN

## Slide 10
LANs, MANs, and WANs
Access Lines
The Network Core
Using the Internet for Wide Area Networking
Cellular Data Service
Virtual WANs

## Slide 11: 10.4: PSTN Local Loop

## Slide 12: 10.4: PSTN Local Loop

## Slide 13: 10.4: PSTN Local Loop

## Slide 14: 10.5: Local Loop Technologies
Purpose | Local Loop Technology | Considerations
Business Local Loop | 2-pair data-grade UTP | For leased lines up to about 2 Mbps Must be pulled to the customer premises Not limited to 100 meters
 | Optical fiber (carrier fiber) | For leased lines more than about 2 Mbps Must be pulled to the customer premises

## Slide 15: 10.5: Local Loop Technologies
Purpose | Local Loop Technology | Considerations
Residential Local Loop | 1-pair voice-grade UTP | Designed only for voice transmission Can be used for digital subscriber line (DSL) service Not limited to 100 meters Already installed; avoids cost of pulling media
 | Optical fiber (carrier fiber) | Fiber to the home New Installed in entire neighborhoods to reduce cost

## Slide 16: 10.5: Local Loop Technologies
Purpose | Local Loop Technology | Considerations
Internal Data Wiring | 4-pair UTP (Category 3-6A) | For inside a site Usually limited to 100 meters
 | Multimode optical fiber | Limited to about 300 meters

## Slide 17: 10.6: Access Lines v Leased Lines

## Slide 18: 10.7: Dial-Up Lines v Leased Lines
Characteristic | Dial-Up Connections | Leased Lines
Connectivity | Point-to-any-point (Any-to-Any) | Point-to-point
Connection Period | Duration of a call | Duration of the lease (always on)
Payment | By the minute for long distance calls | Flat rate plus per-use changers
Commitment | None (except for cellular plans) | Duration of the lease
Data Transmission Speed | Low to moderate | Moderate to high

## Slide 19: 10.8: Leased Line Speeds
North American Digital Hierarchy |  | 
T1 | 1.544 Mbps | 2-Pair Data-Grade UTP
Fractional T1 | 128 kbps, 256 kbps, 384 kbps, 512 kbps, 768 kbps | 2-Pair Data-Grade UTP
Bonded T1s (multiple T1s acting as a single line) | Small multiples of 1.544 Mbps | 2-Pair Data-Grade UTP
T3 | 44.736 Mbps | Carrier Optical Fiber

## Slide 20: 10.8: Leased Line Speeds
CEPT Hierarchy (Europe) |  | 
Fractional E1 |  | 2-Pair Data-Grade UTP
E1 | 2.048 Mbps | 2-Pair Data-Grade UTP
Bonded E1 | Small multiples of 2.048 Mbps | 2-Pair Data-Grade UTP
E3 | 34.368 Mbps | Carrier Optical Fiber

## Slide 21: 10.8: Leased Line Speeds
SONET/SDH Speeds |  | 
OC3/STM1 | 155.52 Mbps | Carrier Optical Fiber
OC12/STM4 | 622.08 Mbps | Carrier Optical Fiber
OC48/STM16 | 2,488.32 Mbps | Carrier Optical Fiber
OC192/STM64 | 9,953.28 Mbps | Carrier Optical Fiber
OC768/STM256 | 39,813.12 Mbps | Carrier Optical Fiber

## Slide 22: 10.9: Digital Subscriber Lines (DSLs)
Feature | ADSL | VHDSL | HSDL | HSDL2 | SHDSL
Name | Asymmet-ric DSL | Very-High-Bit- Rate DSL | High-Rate Symmetric DSL | High-Rate Symmetric DSL Version 2 | Super-High Rate Symmetric DSL
Uses existing 1-pair VG UTP? | Yes* | Yes* | Yes* | Yes* | Yes*
Target Market | Residences | Residen- tial multi-tenent buildings | Business | Business | Business
* Duh. That’s the definition of DSLs.

## Slide 23: 10.9: Digital Subscriber Lines (DSLs)
Feature | ADSL | VHDSL | HSDL | HSDL2 | SHDSL
Down-stream | Initially, 1.5 Mbps; now up to 12 Mbps | 52 to 100 Mbps | 768 kbps | 1.544 Mbps | 384 kbps to 2-3 Mbps
Upstream | Initially, up to 0.5 Mbps; now up to 3.3 Mbps | 16 to 100 Mbps | 768 kbps | 1.544 Mbps | 384 kbps to 2-3 Mbps
Speed Symmetry? | No | Yes or No | Yes | Yes | Yes
QoS SLA? | No | No | Yes | Yes | Yes

## Slide 24: 10.10: Asymmetric Digital Subscriber Line (DSL) Service

## Slide 25: 10.10: Asymmetric Digital Subscriber Line (DSL) Service

## Slide 26: 10.10: Asymmetric Digital Subscriber Line (DSL) Service
DSLAM = DSL Access Multiplexer

## Slide 27: Cable Modem Service
Coaxial cable service was created to bring television to homes that had poor over-the- air reception
Now also offers two-way data service called cable modem service
Popular in the United States
Not popular in most countries

## Slide 28: 10.12: Coaxial Cable
Two conductors: central wire and coaxial ring

## Slide 29: 10.11: Cable Modem Service

## Slide 30: 10.11: Cable Modem Service

## Slide 31: ADSL versus Cable Modem Service
In general …
Cable modem service offers somewhat faster individual throughput at a somewhat higher cost.
ADSL service offers somewhat slower individual throughput at a somewhat lower cost.

## Slide 32
LANs, MANs, and WANs
Access Lines
The Network Core
Using the Internet for Wide Area Networking
Cellular Data Service
Virtual WANs

## Slide 33: 10.13: Leased Line Data Network

## Slide 34: 10.14: Public Switched Data Network (PSDN)

## Slide 35: 10.15: Switched Data Network Standards
X.25
  1970s technology
  Slow and expensive
  Gone today
Frame Relay
ATM
Metropolitan Area Ethernet

## Slide 36: 10.15: Switched Data Network Standards
Frame Relay
  Started to grow in the 1990s
    Inexpensive and fast compared to X.25
    256 kbps to about 40 Mbps
    This is the range of greatest corporate demand for WAN speeds

## Slide 37: 10.15: Switched Data Network Standards
Frame Relay
  Grew rapidly in the 1990s thanks to low prices
  Took market share away from leased line corporate networks
  Carriers have raised their prices to improve profit margins
    This has reduced growth
    Many companies are going back to leased lines for many links

## Slide 38: 10.15: Switched Data Network Standards
ATM
  Much higher speeds than Frame Relay, at much higher prices
    Speeds of 1 Mbps to gigabits per second
    Adoption for PSDN service has been limited
  Created to replace the core of the Public Switched Telephone Network
    Widely adopted for the Public Switched Telephone Network core

## Slide 39: 10.15: Switched Data Network Standards
Metropolitan Area Ethernet
  Metropolitan area network (MAN): city &environs
  Smaller distances than national or international WANs, so lower prices and higher speeds
  Speeds of 1 Mbps to 100 Mbps
  No learning is needed because all firms are familiar with Ethernet
  Carrier can provision or re-provision service speed rapidly, giving flexibility
  The only PSDN service growing rapidly

## Slide 40: 10.16: Virtual Circuit Operation
Box

## Slide 41: 10.16: Virtual Circuit Operation
Box

## Slide 42: 10.16: Virtual Circuit Operation
Box

## Slide 43
LANs, MANs, and WANs
Access Lines
The Network Core
Using the Internet for Wide Area Networking
Cellular Data Service
Virtual WANs

## Slide 44: 10.17: Using the Internet for Wide Area Networking
The Internet is a Wide Area Network
  Many corporations are beginning to use the Internet for some part of their WAN traffic.
  In the future, the Internet is likely to carry most corporate site-to-site traffic and other WAN traffic.

## Slide 45: 10.17: Using the Internet for Wide Area Networking
Attractions
  The price per bit transmitted is very low because of large economies of scale.
  All corporate sites, employees, customers, suppliers, and other business partners are connected to the Internet.
Issues
  The security of traffic flowing over the Internet
  Variable quality of service, with no guarantees

## Slide 46: Securing the Internet
Border firewall at each site
Virtual private networks
  IPsec encryption for sensitive information
  SSL/TLS for less sensitive information
Antivirus filtering

## Slide 47: 10.18: Connecting All Corporate Sites to a Single ISP
If all sites connect to a single ISP, the ISP can provide QoS guarantees.

## Slide 48
LANs, MANs, and WANs
Access Lines
The Network Core
Using the Internet for Wide Area Networking
Cellular Data Service
Virtual WANs

## Slide 49: 10.19: Cellular Technology

## Slide 50: 10.20: Cellsite for Mobile Telephones
Cellsite
Cellular
Antennas
Point-to-Point Microwave
Antenna to MTSO

## Slide 51: 10.19: Cellular Technology

## Slide 52: 10.21: Cellular Technology
Channel Reuse
  The same channel can be used in multiple cells.
    This allows subscribers to use the same channel if they are in different sites.
    Consequently, the carrier can serve more customers per channel.

## Slide 53: 10.21: Cellular Technology
Channel Reuse
  Channel reuse in adjacent cells
    The concern is interference between cellsites and customers using the same channel in adjacent cells.
    Some cellular technologies allow channel reuse in adjacent cells, others do not.

## Slide 54: 10.21: Cellular Technology
Channel Reuse
  Example without channel reuse:
    500 channels, so only 500 simultaneous subscribers can be served
    Channel reuse factor (varies): 20
    Number of simultaneous calls supported: 10,000

## Slide 55: 10.19: Cellular Technology

## Slide 56: 10.22: Handoff and Roaming in 802.11 and Cellular Networks
 | Handoff | Roaming | Mean the Same Thing?
802.11 | From one access point to another | From one access point to another | Yes
Cellular telephony | From one cellsite to another within the same carrier’s system in a city | From a system in one city to a carrier system in another city | No

## Slide 57: 10.23: Generations of Cellular Service
Cellular telephony has gone through several technological generations.
Generation 1 (1G)
  1980s
  Analog signaling
  Data transmission difficult, limited to 10 kbps

## Slide 58: 10.23: Generations of Cellular Service
Generation 2 (2G)
  1990s
  Digital signaling
  Data transmission easier but still limited to 10 to 20 kbps
  Sufficient for texting

## Slide 59: 10.23: Generations of Cellular Service
Generation 3 (3G)
  Around 2001
  Requirement to give at least 2 Mbps download speeds to stationary customers
  Requirement to give at least 384 kbps download speeds to moving customers
  Throughput far lower in practice initially, typically about 100 to 500 kbps stationary but still far higher than 2G

## Slide 60: 10.23: Generations of Cellular Service
Generation 3 (3G)
  Created an explosion in data use.
  Web surfing, streaming video, file synchronization, and so on are possible.
  Soon, some laptop computers used 3G service.
  Eventually, tablets and other devices used 3G.
  Cellular service was not just for phones anymore.

## Slide 61: 10.23: Generations of Cellular Service
Generation 4 (4G)
  Speed Requirements
    Designed to give at least 1 Gbps download speeds to stationary customers
    Designed to give at least 200 Mbps download speeds to moving customers
    Makes wireless as good as or better than wired Internet access
    Sufficient for heavy Web downloading
    Sufficient for high-quality streaming video

## Slide 62: 10.23: Generations of Cellular Service
Generation 4 (4G)
  Technical Characteristics
    Uses IP, typically IPv6
    MIMO
    Scalable bandwidth 5 to 20 MHz
      From high but economical speeds to ultrahigh speeds
    Strong quality of service management

## Slide 63: Today: Closing the Gap
3G systems grew well beyond the initial requirements.
2013: two services are dominant
  HSPA+ (High-Speed Packet Access)
    42 Mbps rated speed in the best systems
    Half that in most
    Actual typical speed is 7 Mbps down, 1 Mbps up
  LTE (Long-Term Evolution)
    Actual typical speed: 10 Mbps down, 6 Mbps up

## Slide 64: Which Services are 4G?
LTE Advanced
  Will be a full 4G service
  Likely to dominate 4G eventually
LTE
  International Telecommunications Union 2010
  Said that precursors of 4G may be called 4G
  This applied to LTE
HSPA+
  Not a precursor to a 4G system, so not a 4G service

## Slide 65: WiMAX
Competitor for LTE
Highly comparable to LTE
Not thriving in the marketplace
Probably a dead-end or niche technology

## Slide 66: 10.24: Lies, Damned Lies, and Service Speeds
Customer Throughput Varies with Many Factors
  Specific technology used (e.g., LTE)
    Specific options used for the technology (very large effect)
    Channel bandwidth
    MIMO or not

## Slide 67: 10.24: Lies, Damned Lies, and Service Speeds
Customer Throughput Varies with Many Factors
  Time of Day
    During the day, there are variations
    More traffic in the day, so slower

## Slide 68: 10.24: Lies, Damned Lies, and Service Speeds
  Customer Location
    Customer is near center or edge of cell (distance hurts)
    Building or terrain obstructions
    In some locations, there may be too few cellsites

## Slide 69: 10.24: Lies, Damned Lies, and Service Speeds
Customer Throughput Varies with Many Factors
  Number of customers sharing the cell at the moment
    Speed decreases approximately linearly with the number of customers
    Whether the carrier minimizes this by having many cells (more expensive for the carrier)

## Slide 70: 10.24: Lies, Damned Lies, and Service Speeds
Customer Throughput Varies with Many Factors
  Smartphone technology and engineering
    Most older smartphones cannot handle the latest carrier offerings at full speed
    They will communicate using a slower older standard

## Slide 71: 10.25: Cellular-802.11 Convergence
Traditional Roles
  802.11 devices received service within a building.
  Mobile phones received cellular service outside.
802.11
Cellular

## Slide 72: 10.25: Cellular-802.11 Convergence
Dual Mode Smartphones
  By default, use cellular network for calls.
  Also connect directly to 802.11 WLANs.
  Customers like this because it gives faster speeds than cellular transmission.
  Customers like this because it helps them stay under their transmission quota limits.
  Cellular companies like offloading traffic from flat-fee users.

## Slide 73: 10.25: Cellular-802.11 Convergence
Some Smartphones Can Act as Access Points
  Provide service to multiple 802.11 devices.
  Carriers charge a premium for this because it adds to their cost.
Cellular
Carrier
ISP
802.11

## Slide 74
LANs, MANs, and WANs
Access Lines
The Network Core
Using the Internet for Wide Area Networking
Cellular Data Service
Virtual WANs

## Slide 75: 10.26: Virtual WANs
Most companies have multiple WAN technology components
  Leased line networks
  PSDNs of different types
  Internet transmission
  Cellular transmission
  Different access link technologies

## Slide 76: 10.26: Virtual WANs
Traditionally, each component has been managed separately.
  However, traffic between hosts often passes through multiple components.
  This makes it difficult to manage overall performance and efficiency.

## Slide 77: 10.26: Virtual WANs
Virtual WAN software provides overall management of the individual WAN components.

## Slide 78: 10.26: Virtual WANs
Virtual WAN software provides overall management of the individual WAN components.
  Allows the overall management of performance and efficiency.
  Individual components can be added, dropped, or changed easily as technology changes.
  It may be possible to simulate the effects of changes before implementation.